## Slide 1: Creating an Actionable Revit Model Diagnostics Tool using Dynamo and Power BI
June 15, 2022
Sean McDonald, Corporate BIM Manager
Kristopher Dane, Director of Digital Design
James Feracor, Digital Design Technologist
Digital Built Week Americas 2022
Anaheim, California
Notes: Learning Objective 2
Ability to utilize that system to accept and track changes through a multi-step update
procedure.
Learning Objective 3
Ability to use Dynamo to pass version and change data to a Revit Master file.
Learning Objective 4
Ability to use Dynamo to check the status of details in an active project against a change
tracking system.

## Slide 2: outline
Introduction (Kris) (10 min)
  Digital Design at Thornton Tomasetti
  Problem
  Solution Outline (James or Sean?)
Live Demo (Kris talk, James control) (10 min)
Deep Dive into Tool Components (40 min)
  Dynamo – Sean (15 min)
  Power BI – James (15 min)
Q/A (James and Sean) 15 mins

## Slide 3: introduction
Develop and drive BIM standards and workflows
Interface between corporate staff (departments) and staff working on projects (practices)
Support IT department to streamline technology infrastructure for client work
Develop workflows and policies for standardizing practices
Evaluate and deploy vendor technologies, software, and services
Improve corporate and staff ability to ‘drive with data’
Digital Design (D2) at Thornton Tomasetti
Notes: Also introduce speakers here

## Slide 4: Problem – NEED DATA, HATE GETTING IT
What’s the Problem?
Checking models is resource intensive!
  Time-consuming, tedious, and inconsistent when performed manually
  Not easy to query / search elements in model using Revit UI… and tons of elements!
Checks yield info valuable in diagnosing potential model issues / measuring model health
Need ability to diagnose model health quickly, consistently, on demand
Digital Design at Thornton Tomasetti
Key questions for models?
  How many sheets do I have, and how many views are on sheets?
  Are objects in the correct worksets?
  How much and what kind of stuff so I have in my model?
  What are the design quantities of the model elements?
  How can I export model data to Excel for further analysis?
  Are the right kinds of things in the right views? According to standards)
How can we answer all these questions automatically for every model, every time?
Notes: Precisely a problem D2 should work on, as automation can really help:
  Minimize data processing time and maximize user time for data consumption/interpretation
This is a classic problem of valuable data existing somewhere
  The process of extraction isn’t inherently difficult
  but is not valuable b/c resource intensive

## Slide 5: Solution walkthrough
We’re going to make solution available to all of you (via GitHub)!
x5
POWER QUERY EDITOR
DATA MODEL + REPORT EDITOR
TASK 1:
Apply Dynamo Scripts to Revit Models
to produce 5 data sets (JSON files)
TASK 2:
Update Power BI Template
to read JSON files + refresh data
TASK 3:
Customize Report for intended end users in Power BI
TASK 4: (Optional)
Improve workflow for repeatability
End users manually trigger Dynamo scripts…
End users consider opportunities to scale + streamline workflow
Power BI Template ingests data automatically!
Notes: Who?
Mins?
JAF: I think sequence should be:
live demonstration of what we built
Main steps for setting up tool
Q&A

## Slide 6: Live Demo
Notes: Who? JF & KD
Mins? 10 mins or more!

## Slide 7: Aspects to cover in the live demo
Report Walkthrough
  Overview Page (Start Here) – summarizes each data set, including warnings and links
  Views/Sheets – Details for sheets and views, including those not on sheets
  Element Data – split into qualitative, quantitative data
Usability Features
  Click items in a visual to filter other visuals on the screen
  Exporter Sheets – make your data modular + accessible
  Export the data from any visual, including filtered results
  Hidden Sheets – Template Pages, Buttons
Notes: @kdane to think about the walk through script
  Make sure that we show that the graphics are linked to gether (click on one)
  Show drill through (clikcon the see “DT Example”)
  I want to know this
  Answer the questions which motivated the problem statement in the Live Demo

## Slide 8: revit model
Notes: Who?
Mins?

## Slide 9: The model
Sample advanced arch (in the folder on teams)
Add worksets
Linked adv struc
Linked basic arch
Broke some things
  Bad link model
  Duplicated objects to get warnings etc.
  Blank sheets etc.
  Some view
Notes: @kdane to add

## Slide 10: Dynamo scripts
POWER QUERY EDITOR
x5
REPORT EDITOR
Notes: Who?
Mins?

## Slide 11: LO1 | Why Dynamo
Why Dynamo
  Its free and installed with Revit
  “Easily” modifiable
Drawbacks to Dynamo
  It can be slow
  It needs to be run manually
  It can be prone to issues
  Issues can be machine specific
  You can’t stop a run without killing Revit

## Slide 12: LO1 | Requirements
Packages
  JsonData Exporting Revit data to JSON
  Archi-lab.net Element selector Linked model info
Sample Files
  Creating using the Autodesk Revit Architecture and Structure sample files (both basic and advanced)
  Modified slightly and linked to make the data export slightly more realistic
Revit
  Sample made using 2022.1.2

## Slide 13: LO1 | the scripts
Script 1: Elements - this is where most data comes from
Script 2: Filedata
- This is where…
Script 3: Links, views, sheets
- This is where./..
Notes: We tried to choose a method that would be easy to understand and modify. Yes, this could be done with fewer nodes or done more efficiently. We tried to make it easy to understand and modify. And … it worked and I got tired of improving it kuz I lazy.

## Slide 14: LO1 | Element Data
Notes: We tried to choose a method that would be easy to understand and modify. Yes, this could be done with fewer nodes or done more efficiently. We tried to make it easy to understand and modify. And … it worked and I got tired of improving it kuz I lazy.

## Slide 15: LO1 script 1 | Element Data
Using archi-lab.net collector to get all model and annotation categories list
Selecting all elements by category using those categories
Flattening and cleaning the list of elements
Notes: Selecting the elements can be done a number of ways.
This is a brute force method. A more targeted method may be beneficial if it will increase the speed of the extraction w/o loss of data that is going to be used.

## Slide 16: LO1 | Element Data
Get all parameters from the list of elements
Convert to string and remove duplicate items
Replace any . with a space (can interfere when exporting)
Notes: Again, this is brute force. A more target selection of parameters may be quicker and still yield the desired results.
Removing the . helped get a more consistent result when exporting
Maintaining the “Levels” becomes very important from this point on

## Slide 17: LO1 | Element Data
Split the parameter fields at the : to get the Parameter and the Value
Using the count of elements in the list, empty values can be filtered out
Both grabbing and removing the elements at index 0 will create the 2 lists (parameters and values)
Notes: The mask by count and get/remove by index 0 is to allow for values that may have been split additional times buy the : in the previous step. Removing items at index 0 also keeps the values list group in the event of the additional splits from the :

## Slide 18: LO1 | Element Data
Join any values that may have been split
Remove any : left in the parameter name
Group all the values by parameter name
Notes: As mentioned previously, values may have been split additional times due to having a : in the value. This will join them. A – was used, again, this yielded less issues than a : when exporting the JSON
In the parameter name, : may be left because we split by space : space. Again these colons are removed to improve the JSON export
Next we need to group the values by the parameter names. This is because we may have several parameters with the same name in the Revit model, but they may have different values. We will be sending this into a dictionary in a later step, so the “keys” need to be unique. Originally, we had played with prefixing the parameter names with their ID. While this did work, it made the data harder to work with and did not improve the quality of the data in any meaningful way. By joining them up with a unique delimiter we can split them back out in PowerBI later if we want to.

## Slide 19: LO1 | Element Data
Join the values for parameters with the same name
Add the element ID and GUID values to the front of each element
Add the elements ID and GUID keys to each parameter list
Notes: Here is where we join those parameters with the same name. We are using a delineator that will be easy to identify, and unlikely to be in any values, in case we need to split them back out later.
Next we are prefixing the list for each element with the GUID and Element ID. These are also added to the “keys”

## Slide 20: LO1 | Element Data
Create a list of all parameters
Create blank values for the list of parameters
Add these to the front of the values and keys lists
Notes: This step was added when we noticed an issue arise with very large models. The JSON file stores the parameters associated with each element. PowerBI takes a sample of the first 1000 elements and builds the parameter list from that sample. If a parameter does not show up in the list by the 1000th item it will not appear in PowerBI. By putting the full list of parameters at the front of the JSON we ensure PowerBI gets them all. This line can be removed in PowerBI once the JSON is loaded.

## Slide 21: LO1 | Element Data
Create a dictionary with the parameter names and parameter values
Grab the dictionary Keys and Values
Notes: We will be using the dictionary to JSON node from the JsonData Package. This created the cleanest results.

## Slide 22: LO1 | Element Data
Create a file name and path string
Notes: To help keep the files easy to identify we are saving them in a consistent path with a preset name prefixed with the data and time.

## Slide 23: LO1 | Element Data
Convert dictionary keys and values to a JSON object
Write out the JSON
Notes: Use the JsonData node for dictionaries to format the JSON and the write JSON node to save the file

## Slide 24: LO1 script 2 | Sheet / View
Select by category for both views and sheets
For views, filter our view templates
Notes: Similar to the elements, selecting all elements by category. Only by manually naming the category. I have found the graph will last longer if you do category by name as opposed to the dropdown (as what shows up in the dropdown will change in different versions).
Views has an additional step of filtering out all the view templates.

## Slide 25: LO1 | Sheet / View
Center of the graph is identical to the elements graph
Notes: This is simply a copy and paste of the guts of the elements graph. Works for both the views and sheets (if it aint broke don’t fix it). Once this section is how you like it, creating a custom node for it may be useful if you want to pull several more JSON exports.
Adding the consolidated list of parameter names was omitted from these graphs since the parameter name will be consistent for all elements in the lists (they are all the same category).

## Slide 26: LO1 | Sheet / View
Create dictionary, create JSON and export are all the same from elements graph
Connected category name to file name
Notes: The conversion and export method is identical to the elements graph as well.
From the file name string generator, it is connected directly to where the category name was written. That way (at least for the sheet version) different categories can be saved simply by typing a new name in that field (view has the extra view template mask).

## Slide 27: LO1 | Links
Most of the links graph is the same as views/sheets
Exceptions
  Get links using archi-lab.net node
  Add the link name and path to parameter list
Notes: Links works just the same as sheets and views. The only exceptions are, to grab the file paths, the archi-lab.net node is used.
Since we are using it, and it is giving all the link instances anyway, we are just passing that to the main body of the graph.
Just before we create the dictionary, we are adding the path parameter name and value back into the elements list.

## Slide 28: LO1 | Warnings
Use GetWarnings node to collect warnings
Extract the severity and descriptions
Reformat the list
Creating dictionary, JSON format, and file export are the same
Notes: Again, similar formatting.
Using the dynamo warning collector extraction nodes to collect the data, reformatting it to be grouped by warning, and adding it to the dictionary.
The dictionary creation, JSON formatting, and file export are exactly the same as the previous examples

## Slide 29: LO1 | Sheet / View / Link / Warnings
To save time, sheets / views / links are in the same graph
Notes: All of these are in the same graph so they can all be run at once. With more complex list manipulation they could be combined. But, as stated previously, I am lazy. Additionally, I have found that complex list manipulation can cause the graph to take much longer to run.
Elements was specifically excluded from these as it alone will take a long time to run. Ran on a large airport project and it took half a day to run the element. All the other graphs combined run in under 5 minutes.

## Slide 30: LO1 | Customizing the Script
Speed
  Limit the extraction to model or annotation elements
  Limit the extraction by category
  (example)
Consistency
  Limit the extraction to specific parameters
  (example)

## Slide 31: LO1 | Expanding the Script
Elements in view
File/ Project level info
Loaded, unplaced content
Overlapping elements
Geometry data
Notes: I selected what I did to extract because it encompassed a lot and was consistent in method. Additionally, apart from a couple of nodes that came from well known packages, there was no custom nodes/python nodes/scripting.
This could very easily be expanded to grab additional data.

## Slide 32: Import data into power bi
POWER QUERY EDITOR
x5
REPORT EDITOR
Notes: Who?
Mins?

## Slide 33: Why power bi?
Desktop
Consistently clean and process model data automatically
Powerful beyond Excel…and Revit UI sucks for analysis
Desktop App is free and comes with most features (try before buying Pro)
Self-service tool empower users, does not require process ownership
Pro (and higher)
Collaborative features - web-based and centralized access (single source of truth)
Integrates well with Microsoft products, especially Teams
Scheduled data refreshes to optimize workflow for end-users
Shifts user focus from processing to consuming and interpreting data

## Slide 34: Preparation Checklist
Check your version of Power BI
Template made w/ May 2022 update
Power BI not backwards compatible, so use this version or later
Organize JSON files into single folder
Turn off Auto-Detect Relationships
Power BI frequently and incorrectly tries to relate tables
Unexpected relationships can over constrain model and create refresh issues
Turn this off (if not already turned off)
File > Options and setting > Options > Current File: Data Load
Before using Power BI template
Notes: Notes re: folder creation
* All files should go in a single folder or subfolder
* If you have extracts from multiple snapshots, I would always call the most recent file the same thing (e.g. ProjectName_Views.json)
* If you want to keep older extracts, recommend prefixing older files with ISO formatted date and move to an archive subfolder, e.g.
(rename file 20220601_ProjectName_Views.json and place in _archive subfolder)

## Slide 35: Anatomy of Power bi
What the developers sees (PQ) versus what the end user sees (report editor)
Report Editor
Define the intended user experience, customize the display of information
Power Query Editor
Transform and optimize the flow of data that all users to consume
‘Process the data so end users don’t have to’
‘Make reports useful and usable’
Model View
Table relationships
Data View
Report View
Intended purpose
Available data as a table
Create and format visuals
Primary Sections in Power BI
Subsections
Advanced knowledge of Power BI not needed to use template… but it can help you further refine it
Notes: Power BI effectively has 4 views, but most are for developers
Power Query Editor
‘If all end users would benefit from a data transformation, it goes here’
Ingest + transform the underlying data sources before visualization
Add/remove columns, combine tables (merge/join, append)
Parameterize file names and manage credentials for source
Create reusable functions
Report Editor, which has 3 sections. Effectively, this is where the user experience is defined in Power BI.
‘In addition to perceived usefulness, reports must also be perceived as usable’
Data Model
Define relationships between tables
This affects how filters/slicers operate on data
Data View
See data available to report as tables
Create calculated tables, columns, and measures
Report Editor
Create and format interactive visualizations
Control usability features (slicers, appearance, interactivity) + aesthetics

## Slide 36: LOAD JSON Data into Power BI
Point the tool to the 5 JSON files in Power Query. Done!
Load more data, perform additional data transformations (e.g. joins, merges, delete unused columns, change column formatting)
New Users:
Advanced Users:
New users only need to load data; advanced users may further customize
Put your JSON files in a folder…
In the Power BI template, there are 6 ‘Parameters’ in Power Query editor you need to provide inputs for:
path_JSON
file_Views
file_Links
file_Warnings
file_Sheets
file_Elements
Notes: Power Query Editor
Basic Users: All you need to do is provide the name and path of your JSON files. That’s it!
Advanced Users: perform additional transformations based on your comfort level
Data Model + Report Editor
Basic Users: Refresh your data. Adjust format of visuals, add/remove columns from tables
Advanced Users: Add new calculations, tables, visualizations; create more advanced usability features

## Slide 37: LOAD JSON Data into Power BI
Point the tool to the 5 JSON files in Power Query. Done!
Load more data, perform additional data transformations (e.g. joins, merges, delete unused columns, change column formatting)
New Users:
Advanced Users:
New users only need to load data; advanced users may further customize
path_JSON
file_Views
file_Links
file_Warnings
file_Sheets
file_Elements
Edit the values to match the name of your JSON file + folder path
Press ‘Load’ when done
You will be prompted to enter these parameters when you open the template for the first time
Notes: Power Query Editor
Basic Users: All you need to do is provide the name and path of your JSON files. That’s it!
Advanced Users: perform additional transformations based on your comfort level
Data Model + Report Editor
Basic Users: Refresh your data. Adjust format of visuals, add/remove columns from tables
Advanced Users: Add new calculations, tables, visualizations; create more advanced usability features

## Slide 38: LOAD JSON Data into Power BI (cont)
(1) Click on a parameter to see its current value in the pane to the right…
(2) …then edit the value to match the name of your JSON file (or folder path)
(4) After updating all [6] parameters, press ‘Close & Apply’ (top left icon)
path_JSON
file_Views
file_Links
file_Warnings
file_Sheets
file_Elements
(3) repeat step for the other 4 JSON files + the parent folder path
If you want to modify the parameters in the future…
ADVANCED TOPIC
Notes: If this isn’t your first time opening the template, then you can also edit the parameters at any time.
You just won’t get the nice prompt in the previous slide.

## Slide 39: LOAD JSON Data into Power BI (Cont)
Query folders are optional, but help you stay organize
Lookups
Main
Intermediates
Parameters
Query Errors
(Optional) for header tables. Can assist with dev
Parameters that allow you to swap while JSON files are loaded into the report (from previous slides)
(Optional) A place to put tables necessary for calculations but not needed for any specific visual. For developers.
Primary data tables used to create model + report visuals
Incoming
(Optional) Folder for new queries while in development or scratch work
Summary of errors that may have occurred when loading your data
ADVANCED TOPIC

## Slide 40: JSON Data Contents
Mapping JSON to Tables
Data Cleaning Steps
Split large tables into components
Clean data for formatting
  truncate multi-values cells
  consistent values
  consistent column headers
  separate units from quantities
Summarize tables for visuals
Optional (but helpful)
Generate lists of column headers to assist with development
ADVANCED TOPIC
Notes: Each JSON file is used to create 1 or more tables:

## Slide 41: CUSTOMIZE POWER BI
POWER QUERY EDITOR
x5
REPORT EDITOR
Notes: Who?
Mins?

## Slide 42: Customize Power BI Report
Use Power BI Report editor to
Two areas of customization to focus on: perceived usefulness, perceived usability
  Perceived Usefulness: How useful is data model + data visualizations?
  Perceived Usability: Can users navigate it on their own?
Use Report Editor to align report content to specific needs of intended end users
Model Considerations
Additional / alternative visualizations (details)
Additional measures, calculated columns, or tables
Key performance metrics
Table relationships (cardinality and direction)
Usability Considerations
Slider syncing / Interactivity features
Tooltips and on-screen guidance
Links to company-specific resources / guidance
Buttons and bookmarks
Notes: NOTE:
Previously, usability really wasn’t a big concern in Excel because developers cannot easily control the user experience
Power BI shifts this tremendously, so now it really matters.
CEs aren’t used to developing interfaces, so this is where manager /stakeholder feedback can really help
Model Considerations
  Additional summary tables + visualizations
  Key performance metrics
Usability Considerations
  Slider Syncing / Interactivity Features
  Additional columns or measures
  Tooltips, resources, and guidance to company-specific content

## Slide 43: IDEAS FOR Customizations
Branding and Aesthetics
Users will find report more useful if it feels relevant to specific needs of company
Display information in manner that end users expect (standard metrics?)
Add tooltips that help users interpret what they see
Report Versioning + Control Complexity
Create alternative versions of pages or reports with different levels of detail
Hide details for casual users, but data available on demand
Add branding and customize aesthetics

## Slide 44: Data MODEL
For developers who want to expand on the template model
Data Model as it exists in the Power BI template
Note that Links and Warnings tables are not connected to the model
Future development could link elements to views and sheets they belong to
New tables based on Elements or Views should be related to their corresponding ‘master’ table
  When creating slicers for views or elements, use the ‘master’ table columns
  This ensures slicers are synced across pages
ADVANCED TOPIC

## Slide 45: Example Customization #1
Query: Which element types have over 200 elements in the model?
Solution: Create calculated table to filter elements table by the number of elements per category, then use as slicer.
Add a calculated table + relate to existing model
summarize_type =
SUMMARIZE(Elements_master,[Type],
"Elements", COUNT(Elements_master[EID])
)
1. Add Calculated Table w/ DAX
2. In Model View, relate summary table to master table on [Type] field (both directions)

## Slide 46: Example Customization #1
Query: Which element types have over 200 elements in the model?
Solution: Create calculated table to filter elements table by the number of elements per category, then use as slicer.
Add a calculated table + relate to existing model
ANSWER:
108 types w/ <200 elements
3 types w/ 200+ elements

## Slide 47: Example Customization #2
Query: What is the distribution of elements by Level for a selected Workset?
Solution: Create drill-through page with specific view user expecting
Add a drill through page
1. Create a new page Make sure it is hidden (I called mine “DT-Example”
2. Under ‘Drill through’:
Turn ‘Keep all Filters’ on
Add ‘Elements_master’[Workset] to filter (MUST be column as table)
Back button automatically created when you add a field to Drill Through

## Slide 48: Example Customization #2
Query: What is the distribution of elements by Level for a selected Workset?
Solution: Create drill-through page with specific view user expecting
Add a drill through page
Dynamically see detailed breakdown of a selected Workset like this
From ‘Element Summary’ page
'Hidden’ Drill Through page (‘DT-Example’)
Right click a Workset, then select ‘Drill Through’
Notes: Lazy Method: Just select it on the template page!

## Slide 49: TRoubleshooting data load
Need another slide for when you want a new parameter that isn’t in the template
Add a drill through page
Notes: Lazy Method: Just select it on the template page!

## Slide 50: Develop your ROADMAP
POWER QUERY EDITOR
x5
REPORT EDITOR
Notes: Who?
Mins?

## Slide 51: Advantages and limitations
Consider the opportunity costs of your deployment
Limitations
Advantages
No publishing, collaboration features
Does not leverage best features of Sharepoint
Sub-optimal workflow for end users, who must refresh data each time (takes time to re-calculate)
Power BI Desktop (Free Only)
Power BI Pro (or higher)
Complex merges cannot be done without Premium level (but there are workarounds!)
JSON files are not centrally managed (no tracking)
Web-based platform, centralized sharing
Dataflows + scheduled refreshes
Collaboration: Publishing, Teams integration
Row-based security, incremental refresh
General Points
Cannot fully automate execution of Dynamo yet
Single model snapshot only; no comparison features
Scripts are self-service, on demand (as needed) Small footprint (just save the JSON files)
Engaging interactive reports, rapid turn-around Ability to add company-specific user guidance
Minimal focus on data processing
re
Automatic, consistent, repeatable data transforms
Source data is unmodified by process
Allow users to export filtered data as needed
Incremental development
ADVANCED TOPICS

## Slide 52: SCALE YOUR WORKFLOW
Develop folder structure and naming system
  Allows Power BI to programmatically find JSON files by version, project, model based on path and file name
  Date stamp older data (YYYYMMDD)
  Separate data from dashboards
  Make most current file name consistent
  Allows for future expansion
How to repeat this analysis consistently, improve workflow automation
{identifier} should uniquely identify model and project corresponding to JSON file
Why do this?
Stronger naming / structure conventions enables tools like Power BI to locate and distinguish JSON files intelligently
Notes: Develop folder structure and naming system
Use Power Automate to automate file transfer
Leverage Automation + Collaboration features of Power BI Pro

## Slide 53: SCALE YOUR WORKFLOW
Publish your Dashboard to a workspace
  Provide users access to workspace
  Provide users persistent link to report (or just have users log in to web platform)
  Pin Power BI report to Microsoft teams
Use dataflows, schedule refreshes
  Pre-calculates data for dashboards to reduce load time for end users (more efficient)
How to repeat this analysis consistently, improve workflow automation
Why do this?
Publishing and refresh automation are among the most useful features of Pro in terms of workflow efficiency and optimizing the end user experience
This template is a good example of where the cost of Power BI Pro is justifiable!
Notes: Overall, the goal here is to reduce the time between data acquisition and data interpretation.
This means avoiding the following as much as possible
Time xferring and renaming files, managing files
Repeating the same calculations each time new data arrives
Finding where a file is stored or logging into a web portal to find a report
Copying data from a static PDF report back to Excel
Forcing end user machines to perform calculations that all users would benefit from

## Slide 54: SCALE YOUR WORKFLOW
Use Power Automate for File Management
  Comes with Office 365 if you have it
  Now allows connections to offline source (with proper credentials)
  Move and rename files based on logic
  Could also be done with Task Scheduler and PowerShell if you have the skills!
  Can be combined with Microsoft Forms to further automatic intake process
How to repeat this analysis consistently, improve workflow automation
Why do this?
Save time and reduce clerical reduce errors by automating data transfer and file renaming tasks
Create an ‘Incoming’ Folder
Establish a new connection to your folder in Power Automate + validate credentials
Create flow logic (not covered in this slide deck):
Trigger if new file added to Incoming folder
Check if files exist in destination folder
  If files exist
    prefix file name with current date in ISO format (YYYYMMDD)
    Move renamed files to _archive folder
  Otherwise
    Move new files from Incoming to destination folder
4. Test flow by dropping off JSON files in Incoming Folder
ADVANCED TOPIC
Notes: Use Power Automate to automate file transfer
Leverage Automation + Collaboration features of Power BI Pro

## Slide 55: FURTHER DEVELOPMENT
Allow report to handle multiple snapshots, models
  You need more data columns that distinguish which model, which snapshot, and which project
  See folder structure recommendations
Key Performance Indices (KPI) – can we summarize a model’s quality with a single number?
  Define thresholds that should cause concern to modeler or BIM manager (e.g. too many line styles? Too many views not on sheets?)
  Metric allows you to track model health over time and across projects/models on demand
What features would be universally beneficial to all users?
ADVANCED TOPIC

## Slide 56: Your homework
Notes: Who?
Mins?

## Slide 57: Your homework
Download file from GitHub Repo (see QR code)
  Power BI Template
  Dynamo Scripts
  Additional Resources for Devs
Do the Preparation Checklist
Run Dynamo on a model
  Save JSON files in a folder
Configure Template
  Update parameters to JSON files + path
Refresh Data!
Optional Next Steps
  Customize Template
  Develop Roadmap
Getting started on your own
GitHub Repo

## Slide 58: What’s in the GitHub Repo?
Power BI reports (where Power BI template is stored)
Power BI Data
  Where you should put your JSON files
  Includes a sample set to help you start
Sample Models (Revit model used in demo)
Dynamo Scripts (Dynamo scripts to be run on Revit models)
Resources
  Handouts and notes
  This slide deck
Table of Contents

## Slide 59: Thank you
Contact info
ThorntonTomasetti.com

## Slide 60: Workshop Summary
Learning Objectives
Create / Execute Dynamo Script on a Revit model
Transform model data using a Power BI template
Customize dashboard to support your needs
Identify potential for workflow automation + scaling
What is this?
Leverage Dynamo and Power BI to produce on-demand, interactive diagnostic reports on the quality of your BIM models.
Notes: Why are We Doing This?
Desire to give BIM managers and modelers have greater visibility of model quality
Time consuming to manually evaluate BIM model quality; Dynamo and Power BI can automate this process quickly + consistently
Self-service; does not depend on some centralized process

## Slide 61: JSON Data Contents
How/why split big tables into smaller ones?
May need to apply 2 sets of filters to get different results simultaneously
Master table allows for centralized slicing of two related tables
Separate data by formatting (quantitative vs qualitative)
ADVANCED TOPIC
Easiest way to invite users to create custom tables
Notes: Each JSON file is used to create 1 or more tables
What did I do to clean the data? The entire transformation history is saved in the template!
You can try to modify the transformations but make sure you save the report state before you do

## Slide 62: Example Customization #3
Query: How many views appear in sheets?
Solution: 3 different ways of getting this, but different use cases!
Add a new measures and calculated columns
Option 1: ‘Lazy* Solution’
1. Use Views_master table
2. Count distinct sheet numbers and view names
3. Use filter to remove “---” from results. Done!
Why is this ‘lazy’?
For this calc to work, we manually set the filter to remove “---”
What if the user wants to see all the views but also see the number of Views on Sheets? Too bad.
What if we just want a single button to quickly filter to views on a sheet (all of them)? Also, too bad.
ADVANCED TOPIC

## Slide 63: Example Customization #3
Query: How many views appear in sheets?
Solution: 3 different ways of getting this, but different use cases!
Add a new measures and calculated columns
Option 2: Column Calc + Measure
Create a calculated column in View_master that indicates Yes/No if a view is on a sheet
Create a measure in View_master that counts rows where [Category] = “Views” and [Sheet Number] is NOT “---”
IsViewOnSheet = IF( Views_master[Sheet Number] <> "---", "Yes", "No“ )
num_views_on_sheets = CALCULATE(
COUNTROWS(Views_master),
FILTER(ALL(Views_master),
Views_master[Category] = "Views" &&
Views_master[Sheet Number] <> "---"
)
)
Do we need both?
Yes, if you want to calculate the total views on sheets REGARDLESS of what filters are selected.
For example, if you filter out Sheet A2, you may want to know the SELECTED number of sheets on views versus the TOTAL number of sheets on views.
ADVANCED TOPIC

## Slide 64: Example Customization #3
Query: How many views appear in sheets?
Solution: 3 different ways of getting this, but different use cases!
Add a new measures and calculated columns
Option 2: Column Calc + Measure
Create a calculated column in View_master that indicates Yes/No if a view is on a sheet
Create a measure in View_master that counts rows where [Category] = “Views” and [Sheet Number] is NOT “---”
When A2 is filtered out, only 6/11 views on sheets remain
YES/NO Column allows us to select ALL views on sheets (rather than individually)
Are there other ways?
Yep! Can create a calculated column in Sheets_master to find the total number of views per sheet (rather than Views_master) table, then add these numbers.
Advantageous b/c it gives you the views PER sheet as a filterable column, rather than a dynamic calculation (which cannot be used as a slicer).
ADVANCED TOPIC

## Slide 65: User Notes
Working with Master Layouts
We’ve provided an array of slide layouts to maintain consistency and ease of use. You can select these layouts when creating a new slide, and you can change the layouts of existing slides as desired (some adjustments may be required after switching layouts). These layouts contain placeholders for images. Clicking the Reset button will restore the default styles and positions of these elements.
Moving Slides Between Documents
Slides pasted from other presentations will assume the new styles of this template unless the Keep Source Formatting option is selected when pasting. Layouts with the same name (such as “Title and Content”) will map to the correct layout in this template. And you can change the layouts of pasted slides to one of the new layouts (some adjustments may be required after switching layouts).
Header/Footer
The master layout contains placeholders for slide number, date and footer. You may add or remove these elements from all, or selected, slides by using the Insert > Header & Footer function.
Updated: September 3, 2021

## Slide 66: User Notes
General Typographic Style
The default styles embedded in this template will meet virtually all your needs in prescribing typographic style. Their consistent use is an important part of the brand. On rare occasions, you may need to create a new style not found in this template. Please keep the following principles in mind:
This template uses the Arial font.
Only use the flush-left, ragged-right format, never justified.
Slide titles and headings should be uppercase and in boldface.
Except for image credits, at 8 pt., the minimum font size should be 18 pt for body.
Refer to the “Color Usage” section for type color.
Lorem ipsum is the industry standard placeholder for copy.
In some layouts, the correct type styles can be achieved by clicking the Increase List Level button on the Home tab:
Color Usage
Follow these suggestions to maintain a consistent visual brand, and to highlight important content without being distracting.
Text Color:
Main body text is R=99 G=102 B=106.
Slide titles and headings are R=0 G=62 B=81.
R=212 G=69 B=29 and R=0 G=163 B=173 may be used sparingly to highlight small portions of important text.
Background Colors:
As a rule, R=0 G=49 B=60 and R=0 G=163 B=173 are the primary, dominant background colors throughout the document, and should be the only colors to appear in large areas.
Accent Colors:
R=212 G=69 B=29 and R=136 G=219 B=223 should be used sparingly, appearing mainly in small graphic elements, charts and graphs.
First level
Second Level
Third Level

## Slide 67: User Notes
Document Grid and Spacing
This document is built with a 12-column grid, with .375” (27 pt.) gutters. This allows for consistent spacing when creating multicolumn layouts. Follow the grid, aligning elements and keeping the spacing between elements as consistent as possible.
To show the gridlines, click the View tab, and then check the Gridlines box.
The Highlight Bar
The orange highlight bar is a unique brand element that distinguishes our brand from others. It is used sparingly – typically one per slide – in conjunction with the slide title or other heading.
To maintain consistency, follow these size and spacing guidelines:
Large Titles
SIZE: .45˝ x .06˝
MARGIN: .25˝
  Small Titles
SIZE: .33˝ x .05˝
MARGIN: .12˝

## Slide 68: Alternate Layout Presentation Title
January 1, 2020
Presenter names, titles
Client
Venue
Notes: The “presenter/Client/Venue” fields are not all required for all presentations. Use as required. For example, if you are presenting at a professional society meeting, include in the “venue” slot the name of the meeting, location and date:
2020 NCSEA Structural Engineering Summit, Las Vegas
And there is, logically, no client. If you are presenting to a client, there is no need to list a venue.

## Slide 69: Section Header

## Slide 70: Our Locations
 | 1,400 Engineers, Architects, Scientists and other Professionals | 
 | Projects in 50 Countries | 
 | 40+ Offices | 
 | 5 Continents | 

## Slide 71: Our Locations
San Francisco
Silicon Valley
Denver
Kansas City
Albuquerque
Phoenix
Dallas
Austin
Houston
San Diego
Los Angeles
Seattle
Tampa
Fort Lauderdale
Miami
Milwaukee
Chicago
Philadelphia
Newark
Washington DC
New York
Hartford
Boston
Portland
 | 1,400 Engineers, Architects, Scientists and other Professionals | 
 | Projects in 50 Countries | 
 | 40+ Offices | 
 | 5 Continents | 
Orlando

## Slide 72: Our Locations
 | 1,400 Engineers, Architects, Scientists and other Professionals | 
 | Projects in 50 Countries | 
 | 40+ Offices | 
 | 5 Continents | 
United Kingdom
London
Romsey
Warrington
Aberdeen
Ballymena
Edinburgh
Bristol

## Slide 73: Our Core Ideology
Our Purpose
Our Values
Our Goal
We embrace challenges to make lasting contributions.
  We are passionate about what we do.
  We see opportunity where others focus on risk.
  We look beyond the obvious to solve the real problem.
  We challenge people to grow.
To be the global driver of change and innovation in our industry.

## Slide 74: ENGINEERING solutions
Acoustics, Noise & Vibration
Aviation
Commercial & Residential
Construction Engineering
Critical Facilities
Cultural & Community
Defense
Education
Energy
Façades
Forensics & Investigations
Government
Healthcare & Research
Hospitality & Gaming
Insurance
Life Sciences
Protective Design & Security
Resilience
Restoration & Renewal
Special Structures
Sports & Public Assembly
Structural Design
Sustainability
Tall & Supertall Buildings
Transportation/Infrastructure

## Slide 75: Agenda
Ideal length of bulleted text is one line
Lorem ipsum.
Lorem ipsum.
Lorem ipsum.
Lorem ipsum.

## Slide 76: INNOVATION OUTPUT
Conferences
Presentations
AIA Webinars
Innovation Tournaments
Hackathons
Master Classes
Workshops
Education
Online Tutorials
TTWiiN
IDEA GENERATION
COLLABORATION &
SHARING
TRAINING
ACCELERATOR
CORE studio & CORE lab initiatives
We believe collaboration amplifies our innovation potential and creates connections that lead to better, more imaginative solutions for our clients.

## Slide 77: solution Layout
 | Placeholder 50 Text | 
 | 1,500 Placeholder Text Here | 
 | 50+ Placeholder | 
 | 5 Placeholder | 

## Slide 78: Project Team
Theresa Curtis, P.E., S.E., LEED AP BD+C
  Vice President & San Francisco Office Co-Director
    Advanced Project Delivery
    Seismic Performance-Based Design
    Structural Analysis & Design

## Slide 79: Text and Image Layout
Ideal length of bulleted text is one line
Lorem ipsum.
Notes: Make photo collage here.

## Slide 80: useful icons
* If you need a custom icon please contact the marketing-communications team and mention “nucleo.”
Notes: These icons are available to grab, resize, and recolor as you see fit. You can change the color by clicking on an icon and adjusting via the “Shape Fill” and Shape Outline” options n the “Home Ribbon”