## Slide 1: Creating an Actionable Revit Model Health Dashboard using Dynamo and Power BI
June 15, 2022
James Feracor, Digital Design Technologist
Sean McDonald, Corporate BIM Manager
Kristopher Dane, Director of Digital Design
Digital Built Week Americas 2022
Anaheim, California

## Slide 2: outline
Introduction
  Digital Design at Thornton Tomasetti
  Speakers
  Problem
  Solution Outline
Live Demo
Deep Dive into Tool Components
  Dynamo
  Power BI
Q/A

## Slide 3: introduction
Digital Design (D2) at Thornton Tomasetti
Why? So project teams can do work that is worth their time; to focus on high value, high impact problems rather than the commodity activities.
Design Practices
Digital Design
Information Technology
Structural Engineering
Construction Engineering
Protective Design
Forensics
Renewal

## Slide 4: introduction
Presenters
Dr. Kristopher Dane
Director of Digital Design
Seattle, WA
Sean McDonald
Corporate BIM Manager
Chicago, IL
Dr. James Feracor
Digital Design Technologist
Seattle, WA
We’re hosting another session tomorrow at 10:45am: 3.2.08 “AirTable for Version Tracking of Revit Details”

## Slide 5: The Problem
Checking Revit models is resource intensive!
  Time-consuming, tedious, and inconsistent when performed manually
  Not easy to query / search elements in model using Revit UI… and tons of elements!
Need ability to diagnose model health quickly, consistently, on demand
Checks yield info valuable in diagnosing potential model issues / measuring model health
Model Review is Hard
  How many sheets do I have?
  How many views are on sheets?
  Are the right kinds of things in the right views?
  Are objects in the correct worksets?
  How much and what kind of stuff so I have in my model?
  What are the design quantities of the model elements?
  Can I dump model data to Excel for further analysis?
Some questions for models

## Slide 6
We’re going to make solution available to all of you (via GitHub)!
THE Solution
x5
POWER QUERY EDITOR
DATA MODEL + REPORT EDITOR
TASK 1:
Dynamo Scripts -> JSON files
TASK 2:
Update Power BI Template
to read JSON files + refresh data
TASK 3:
Customize Report for intended end users in Power BI
TASK 4: (Optional)
Improve workflow for repeatability
User manually triggers Dynamo scripts…
End users consider opportunities to scale + streamline workflow
Power BI Template ingests data automatically!

## Slide 7: Live Demo

## Slide 8: revit model

## Slide 9: The model
Revit Sample Models

## Slide 10: Dynamo scripts
POWER QUERY EDITOR
x5
REPORT EDITOR

## Slide 11: Why Dynamo
Why Dynamo
  Its free and installed with Revit
  “Easily” modifiable
Drawbacks to Dynamo
  It can be slow
  It needs to be run manually
  It can be prone to issues
  Issues can be machine specific
  You can’t stop a run without killing Revit

## Slide 12: Requirements
Packages
  JsonData Exporting Revit data to JSON
  Archi-lab.net Element selector Linked model info
Sample Files
  Creating using the Autodesk Revit Architecture and Structure sample files (both basic and advanced)
  Modified slightly and linked to make the data export slightly more realistic
Revit
  Sample made using 2022.1.2

## Slide 13: the scripts
Script 1: Elements
Script 2: Links, views, sheets, warnings

## Slide 14: script 1 | Element Data
Using archi-lab.net collector to get all model and annotation categories list
Selecting all elements by category using those categories
Flattening and cleaning the list of elements

## Slide 15: script 1 | Element Data
Get all parameters from the list of elements
Convert to string and remove duplicate items

## Slide 16: script 1 | Element Data
Split the parameter fields at the : to get the Parameter and the Value
Using the count of elements in the list, empty values can be filtered out
Both grabbing and removing the elements at index 0 will create the 2 lists (parameters and values)

## Slide 17: script 1 | Element Data
Join any values that may have been split
Remove any : left in the parameter name
Group all the values by parameter name

## Slide 18: script 1 | Element Data
Join the values for parameters with the same name
Add the element ID and GUID values to the front of each element
Add the elements ID and GUID keys to each parameter list

## Slide 19: script 1 | Element Data
Create a list of all parameters
Create blank values for the list of parameters
Add these to the front of the values and keys lists

## Slide 20: script 1 | Element Data
Create a dictionary with the parameter names and parameter values
Grab the dictionary Keys and Values

## Slide 21: script 1 | Element Data
Create a file name and path string

## Slide 22: script 1 | Element Data
Convert dictionary keys and values to a JSON object
Write out the JSON

## Slide 23: script 2 | Sheet / View
Select by category for both views and sheets
For views, filter our view templates

## Slide 24: script 2 | Sheet / View
Center of the graph is identical to the elements graph

## Slide 25: script 2 | Sheet / View
Create dictionary, create JSON and export are all the same from elements graph
Connected category name to file name

## Slide 26: script 2 | Links
Most of the links graph is the same as views/sheets
Exceptions
  Get links using archi-lab.net node
  Add the link name and path to parameter list

## Slide 27: script 2 | Warnings
Use GetWarnings node to collect warnings
Extract the severity and descriptions
Reformat the list
Creating dictionary, JSON format, and file export are the same

## Slide 28: script 3 | All
For ease of use all the scripts can be combined

## Slide 29: script 2 | Customizing the Script
Speed
  Limit the extraction to model or annotation elements
  Limit the extraction by category
Consistency
  Limit the extraction to specific parameters

## Slide 30: Expanding the Script(s)
Elements in view
File/ Project level info
Loaded, unplaced content
Overlapping elements
Geometry data

## Slide 31: Import data into power bi
POWER QUERY EDITOR
x5
REPORT EDITOR
…as an end-user

## Slide 32: Why power bi?
Desktop
Consistently clean and process model data automatically
Powerful beyond Excel…and Revit UI sucks for analysis
Desktop App is free and comes with most features (try before buying Pro)
Self-service tool empower users, does not require process ownership
Pro (and higher)
Collaborative features - web-based and centralized access (single source of truth)
Integrates well with Microsoft products, especially Teams and Sharepoint
Scheduled data refreshes to optimize workflow for end-users
Shifts focus from processing to consuming / interpreting data
TT delivers data via Power BI platform

## Slide 33: Preparation Checklist
Check your version of Power BI
Template made w/ May 2022 update
Power BI not backwards compatible for this version, so must use this version or later
Organize JSON files into single folder
Turn off Auto-Detect Relationships
Power BI frequently and incorrectly tries to relate tables
Unexpected relationships can over constrain model and create refresh issues
Turn this off (if not already turned off)
File > Options and setting > Options > Current File: Data Load
When using Power BI template…

## Slide 34: Anatomy of Power bi
What the developers sees (PQ) versus what the end user sees (report editor)
Report Editor
Define the intended user experience,
customize the display of information
Power Query Editor
Transform and optimize the flow of data that all users will consume
Process data so end users don’t have to
Make reports useful and usable
Model View
Table relationships
Data View
Report View
Intended purpose
Available data as a table
Create and format visuals
Primary Sections in Power BI
Subsections
End-User / Consumer
Developer
Roles

## Slide 35: LOAD JSON Data into Power BI
Point the tool to the 5 JSON files in Power Query. Done!
Load more data, perform additional data transformations (e.g. joins, merges, delete unused columns, change column formatting)
New Users:
Advanced Users:
New users only need to load data; advanced users may further customize
Put your JSON files in a folder…
In the Power BI template, there are 6 ‘Parameters’ in Power Query editor you need to provide inputs for:
path_JSON
file_Views
file_Links
file_Warnings
file_Sheets
file_Elements

## Slide 36: LOAD JSON Data into Power BI (cont.)
Point the tool to the 5 JSON files in Power Query. Done!
Load more data, perform additional data transformations (e.g. joins, merges, delete unused columns, change column formatting)
New Users:
Advanced Users:
New users only need to load data; advanced users may further customize
path_JSON
file_Views
file_Links
file_Warnings
file_Sheets
file_Elements
Edit the values to match the name of your JSON file + folder path
Press ‘Load’ when done
You will be prompted to enter these parameters when you open the template for the first time

## Slide 37: LOAD JSON Data into Power BI (cont)
(1) Click on a parameter to see its current value in the pane to the right…
(2) …then edit the value to match the name of your JSON file (or folder path)
(4) After updating all [6] parameters, press ‘Close & Apply’ (top left icon)
path_JSON
file_Views
file_Links
file_Warnings
file_Sheets
file_Elements
(3) repeat step for the other 4 JSON files + the parent folder path
If you want to modify the parameters in the future…
ADVANCED TOPIC

## Slide 38: LOAD JSON Data into Power BI (Cont)
Query folders are optional, but help you stay organize
Lookups
Main
Intermediates
Parameters
Query Errors
(Optional) for header tables. Can assist with dev
Parameters that allow you to swap while JSON files are loaded into the report (from previous slides)
(Optional) A place to put tables necessary for calculations but not needed for any specific visual. For developers.
Primary data tables used to create model + report visuals
Incoming
(Optional) Folder for new queries while in development or scratch work
Summary of errors that may have occurred when loading your data
ADVANCED TOPIC

## Slide 39: JSON Data Contents
Mapping JSON to Tables
Data Cleaning Steps
Split large tables into components
Clean data for formatting
  truncate multi-values cells
  consistent values
  consistent column headers
  separate units from quantities
Summarize tables for visuals
Optional (but helpful)
Generate lists of column headers to assist with development
ADVANCED TOPIC

## Slide 40: Why do we need to transform data?
Transformations pre-programmed in the template make data tables modular
Steps for Elements_master
1. Load raw data
2. Create duplicate for Elements_explore
3. Remove all other columns except GUID or EID and any columns to be used as slicers for Views
4. Filter any rows not needed
ADVANCED TOPIC
Steps for Elements_explore
Remove all columns used in Elements_master except for GUID or EID
(optional) Reformat columns (e.g. change formats to numbers, separate units from quantities, split, etc.)
(optional) Filter any rows not needed
(optional) replace values for consistency (handle blanks, nulls, white spaces)
All tables based on Elements should be connected to Elements_master via [EID]

## Slide 41: CUSTOMIZE POWER BI
POWER QUERY EDITOR
x5
REPORT EDITOR

## Slide 42: Customize Power BI Report
Use Power BI Report editor to
Two areas of customization to focus on: perceived usefulness, perceived usability
  Perceived Usefulness: How useful is data model + data visualizations?
  Perceived Usability: Can users navigate it on their own?
Use Report Editor to align report content to specific needs of intended end users
Model Considerations
Additional / alternative visualizations (details)
Additional measures, calculated columns, or tables
Key performance metrics
Table relationships (cardinality and direction)
Usability Considerations
Slider syncing / Interactivity features
Tooltips and on-screen guidance
Links to company-specific resources / guidance
Buttons and bookmarks

## Slide 43: IDEAS FOR Customizations
Branding and Aesthetics
Users will find report more useful if it feels relevant to specific needs of company
Display information in manner that end users expect (standard metrics?)
Add tooltips that help users interpret what they see
Report Versioning + Control Complexity
Create alternative versions of pages or reports with different levels of detail
Hide details for casual users, but data available on demand
Add branding and customize aesthetics

## Slide 44: Data MODEL
For developers who want to expand on the template model
Data Model as it exists in the Power BI template
Note that Links and Warnings tables are not connected to the model
Future development could link elements to views and sheets they belong to
New tables based on Elements or Views should be related to their corresponding ‘master’ table
  When creating slicers for views or elements, use the ‘master’ table columns
  This ensures slicers are synced across pages
ADVANCED TOPIC

## Slide 45: Example Customization #1
Query: Which element types have over 200 elements in the model?
Solution: Create calculated table to filter elements table by the number of elements per category, then use as slicer.
Add a calculated table + relate to existing model
summarize_type =
SUMMARIZE(Elements_master,[Type],
"Elements", COUNT(Elements_master[EID])
)
1. Add Calculated Table w/ DAX
2. In Model View, relate summary table to master table on [Type] field (both directions)

## Slide 46: Example Customization #1
Query: Which element types have over 200 elements in the model?
Solution: Create calculated table to filter elements table by the number of elements per category, then use as slicer.
Add a calculated table + relate to existing model
ANSWER:
108 types w/ <200 elements
3 types w/ 200+ elements

## Slide 47: Example Customization #2
Query: What is the distribution of elements by Level for a selected Workset?
Solution: Create drill-through page with specific view user expecting
Add a drill through page
1. Create a new page Make sure it is hidden (I called mine “DT-Example”
2. Under ‘Drill through’:
Turn ‘Keep all Filters’ on
Add ‘Elements_master’[Workset] to filter (MUST be column as table)
Back button automatically created when you add a field to Drill Through

## Slide 48: Example Customization #2
Query: What is the distribution of elements by Level for a selected Workset?
Solution: Create drill-through page with specific view user expecting
Add a drill through page
Dynamically see detailed breakdown of a selected Workset like this
From ‘Element Summary’ page
'Hidden’ Drill Through page (‘DT-Example’)
Right click a Workset, then select ‘Drill Through’

## Slide 49: Develop your ROADMAP
POWER QUERY EDITOR
x5
REPORT EDITOR

## Slide 50: Advantages and limitations
Consider the opportunity costs of your deployment
Limitations
Advantages
No publishing, collaboration features
Does not leverage best features of Sharepoint
Sub-optimal workflow for end users, who must refresh data each time (takes time to re-calculate)
Power BI Desktop (Free Only)
Power BI Pro (or higher)
Complex merges cannot be done without Premium level (but there are workarounds!)
JSON files are not centrally managed (no tracking)
Web-based platform, centralized sharing
Dataflows + scheduled refreshes
Collaboration: Publishing, Teams integration
Row-based security, incremental refresh
General Points
Cannot fully automate execution of Dynamo yet
Single model snapshot only; no comparison features
Scripts are self-service, on demand Small footprint (JSON files)
Engaging interactive reports, rapid turn-around
Ability to add company-specific user guidance
Minimal focus on data processing
re
Automatic, consistent, repeatable transformations
Source data unmodified by process
Allow users to export filtered data as needed
Incremental development
ADVANCED TOPICS

## Slide 51: Structure your files and folders
Develop folder structure and naming system
  Allows Power BI to programmatically find JSON files by version, project, model based on path and file name
  Date stamp older data (YYYYMMDD)
  Separate data from dashboards
  Make most current file name consistent
  Allows for future expansion
How to repeat this analysis consistently, improve workflow automation
{identifier} should uniquely identify model and project corresponding to JSON file
Why do this?
Stronger naming / structure conventions enables tools like Power BI to locate and distinguish JSON files intelligently

## Slide 52: Publish and Share
Publish your Dashboard to a workspace
  Provide users access to workspace
  Provide users persistent link to report (or just have users log in to web platform)
  Pin Power BI report to Microsoft teams
How to repeat this analysis consistently, improve workflow automation
Why do this?
Publishing and refresh automation are among the most useful features of Pro in terms of workflow efficiency and optimizing the end user experience
This template is a good example of where the cost of Power BI Pro is justifiable!
Use dataflows, schedule refreshes
  Pre-calculates data for dashboards to reduce load time for end users (more efficient)

## Slide 53: Leverage Power Automate
Use Power Automate for File Management
  Comes with Office 365 if you have it
  Now allows connections to offline source (with proper credentials)
  Move and rename files based on logic
  Could also be done with Task Scheduler and PowerShell if you have the skills!
  Can be combined with Microsoft Forms to further automatic intake process
How to repeat this analysis consistently, improve workflow automation
Why do this?
Save time and reduce clerical reduce errors by automating data transfer and file renaming tasks
Create an ‘Incoming’ Folder
Establish a new connection to your folder in Power Automate + validate credentials
Create flow logic (not covered in this slide deck):
Trigger if new file added to Incoming folder
Check if files exist in destination folder
  If files exist
    prefix file name with current date in ISO format (YYYYMMDD)
    Move renamed files to _archive folder
  Otherwise
    Move new files from Incoming to destination folder
4. Test flow by dropping off JSON files in Incoming Folder
ADVANCED TOPIC

## Slide 54: FURTHER DEVELOPMENT
Allow report to handle multiple snapshots, models
  You need more data columns that distinguish which model, which snapshot, and which project
  See folder structure recommendations
Key Performance Indices (KPI) – can we summarize a model’s quality with a single number?
  Define thresholds that should cause concern to modeler or BIM manager (e.g. too many line styles? Too many views not on sheets?)
  Metric allows you to track model health over time and across projects/models on demand
What features would be universally beneficial to all users?
ADVANCED TOPIC

## Slide 55: Your homework

## Slide 56: Your homework
Download file from GitHub Repo (see QR code)
  Power BI Template
  Dynamo Scripts
  Additional Resources for Devs
Do the Preparation Checklist
Run Dynamo on a model
  Save JSON files in a folder
Configure Template
  Update parameters to JSON files + path
Refresh Data!
Optional Next Steps
  Customize Template
  Develop Roadmap
Getting started on your own
GitHub Repo

## Slide 57: What’s in the GitHub Repo?
Power BI reports (where Power BI template is stored)
Power BI Data
  Where you should put your JSON files
  Includes a sample set to help you start
Sample Models (Revit model used in demo)
Dynamo Scripts (Dynamo scripts to be run on Revit models)
Resources
  Handouts / Notes
  This slide deck
Table of Contents

## Slide 58: Thank you
Contact info
ThorntonTomasetti.com

## Slide 59: JSON Data Contents
How/why split big tables into smaller ones?
May need to apply 2 sets of filters to get different results simultaneously
Master table allows for centralized slicing of two related tables
Separate data by formatting (quantitative vs qualitative)
ADVANCED TOPIC
Easiest way to invite users to create custom tables

## Slide 60: Data loading issues
Elements_geometry, Elements_explore, or summarize_geometry tables are loading data incorrectly
Template tries to generalize steps, but your model contains attributes not included in template (particularly quantitative values)
Issue
Explanation
To fix Elements_geometry…
In the step, 'Removed Columns', make sure that the column you are looking for was not removed
ADVANCED TOPIC
If the column has both units and value in the cell, you will need to split this column by a delimiter (usually a space), then rename the columns…

## Slide 61: Data loading issues (cont.)
Elements_geometry, Elements_explore, or summarize_geometry tables are loading data incorrectly
Issue
To fix Summarize_geometry
Insert step after the 'Filtered Rows' step to remove any rows that you do not want to appear in the summary list
ADVANCED TOPIC
Add a new 'Unpivot Columns' step and unpivot only the columns you want to be summarized, then delete the old 'Unpivot Columns' step
Split the columns as needed to separate units from the value (cannot do math otherwise) + remove any remaining unwanted columns or rows

## Slide 62: Data loading issues (cont.)
Power BI is looking for a column that does not exist in the JSON files
Issue
ADVANCED TOPIC
Power BI is trying to generalize steps from the template to your specific data, but certain columns are missing from the JSON file
Explanation
How to Fix?
(Recommended) add a new column to the JSON file; this will allow Power BI to continue, but the column values will be all empty
Better than trying to find every instance of it in Power BI…

## Slide 63: Data loading issues (cont.)
Dyanmo files updated to add new data, but Power BI doesn't recognize new columns in Element-related tables
Issue
ADVANCED TOPIC
Template does not include the new columns, so it will simply skip importing them.
Explanation
How to fix:
Edit all table queries prefixed with Elements_ in PQ Editor. In the Advanced Editor within PQE:
…
In Advanced Editor within the 'Expanded Column' step, add the new column name at the end of the comma-separated list
Add/remove rows or columns as necessary
(add column name at the end, e.g.
… “z Offset Value”, “NewColumnName”}

## Slide 64: Example Customization #3
Query: How many views appear in sheets?
Solution: 3 different ways of getting this, but different use cases!
Add a new measures and calculated columns
Option 1: ‘Lazy* Solution’
1. Use Views_master table
2. Count distinct sheet numbers and view names
3. Use filter to remove “---” from results. Done!
Why is this ‘lazy’?
For this calc to work, we manually set the filter to remove “---”
What if the user wants to see all the views but also see the number of Views on Sheets? Too bad.
What if we just want a single button to quickly filter to views on a sheet (all of them)? Also, too bad.
ADVANCED TOPIC

## Slide 65: Example Customization #3
Query: How many views appear in sheets?
Solution: 3 different ways of getting this, but different use cases!
Add a new measures and calculated columns
Option 2: Column Calc + Measure
Create a calculated column in View_master that indicates Yes/No if a view is on a sheet
Create a measure in View_master that counts rows where [Category] = “Views” and [Sheet Number] is NOT “---”
IsViewOnSheet = IF( Views_master[Sheet Number] <> "---", "Yes", "No“ )
num_views_on_sheets = CALCULATE(
COUNTROWS(Views_master),
FILTER(ALL(Views_master),
Views_master[Category] = "Views" &&
Views_master[Sheet Number] <> "---"
)
)
Do we need both?
Yes, if you want to calculate the total views on sheets REGARDLESS of what filters are selected.
For example, if you filter out Sheet A2, you may want to know the SELECTED number of sheets on views versus the TOTAL number of sheets on views.
ADVANCED TOPIC

## Slide 66: Example Customization #3
Query: How many views appear in sheets?
Solution: 3 different ways of getting this, but different use cases!
Add a new measures and calculated columns
Option 2: Column Calc + Measure
Create a calculated column in View_master that indicates Yes/No if a view is on a sheet
Create a measure in View_master that counts rows where [Category] = “Views” and [Sheet Number] is NOT “---”
When A2 is filtered out, only 6/11 views on sheets remain
YES/NO Column allows us to select ALL views on sheets (rather than individually)
Are there other ways?
Yep! Can create a calculated column in Sheets_master to find the total number of views per sheet (rather than Views_master) table, then add these numbers.
Advantageous b/c it gives you the views PER sheet as a filterable column, rather than a dynamic calculation (which cannot be used as a slicer).
ADVANCED TOPIC